Example of the edited subset from Segal program:

# Edit boundary from 6.913 to 7.148 we got MW=59KD from Segal program

Selected points                   72

Mid of radial part                7.031

Mid conc                              0.472

Slope                                  0.8933

#### Correlation                         0.999407

# MW, kD                                59.0

Example of edited subset from Beckman Origin:

SE experiment. Sample in:      Running speed: 16K    Running temp:20 0C Use XLA-

59KD from Segal and 66.6KD from origin  using exactly the same radius region. Why?

Is discrepancy of 4-14% acceptable?

Summary: Compare 4 edited subset data from raw data 00008.ra1 using Origin vs. Segal.

| Edit Equilibrium curve | Boundary radius region used | MW obtained from Origin / variance | MW obtained from Segal / correlation | Discrepancy@ % |
| --- | --- | --- | --- | --- |
| Edit 1 | 6.913-7.148 | 67 KD / 17.1 | 59 KD / 0.999458 | 12 |
| Edit 2 | 6.942-7.139 | 66KD / 18.3 | 60 KD / 0.999504 | 9 |
| Edit 3 | 6.920-7.139 | 65 KD / 17.8 | 56 KD / 0.999322 | 14 |
| Edit 4 | 6.897-7.118 | 56 KD / 13.1 | 54 KD / 0.999435 | 4 |

@ (MW obtained from Origin  -  MW obtained from Segal) / MW obtained from Origin

Using default rho(1.006) and v-bar(0.73) for comparison.