Few examples:

Selected points                   82

Mid of radial part                6.836

Mid conc                              0.377

Slope                                  0.6256

Correlation                         0.999972

MW, kD                                87.4  Selected points                   83

Mid of radial part                6.967

Mid conc                              1.394

Slope                                  0.5885

Correlation                         0.999876

MW, kD                                82.2

Summary: Compare 4 edited subset data from raw data 00005.ra1 using Origin vs. Segal.

| Edit Equilibrium curve | Boundary radius region used | MW obtained from Origin / variance (Confidence limit) | MW obtained from Segal / correlation | Discrepancy@ % |
| --- | --- | --- | --- | --- |
| Edit 1 | 6.806-7.112 | 82KD / 11.8 (79-84KD) | 82 KD / 0.999876 | 0 |
| Edit 2 | 6.685-6.984 | 86KD / 4.6 (83-89KD) | 87 KD / 0.999972 | -1.2 |
| Edit 3 | 6.831-7.076 | 81KD / 11.6 (77-84KD) | 83KD / 0.999018 | -2.5 |
| Edit 4 | 6.689-6.975 | 89KD / 4.1 (85-92KD) | 89KD / 0.999959 | 0 |

@ (MW obtained from Origin  -  MW obtained from Segal) / MW obtained from Origin

Using default rho(1.006) and v-bar(0.73) for comparison.

Use default V-bar=0.73 , rho=1.006