### MW=295052, with a sub set radius range ~ 6.9 to 7.12 cm, variance =0.68076

MW=283415, with a sub set radius range ~ 6.9 to 7.12 cm, variance =0.61974

MW=369996, with a sub set radius range ~ 6.9 to 7.15 cm, variance =1.40996

Self-association model searching: To be consistence, I select subset radius range from 6.9-7.12 cm for the following guess work using variance as a guide to arrive at the final conclusion.

**************************************************************************************

## Monomer to Trimer, with a variance=0.7347 and Ka3=6.98E78

## Monomer to Tetramer, with a variance=0.61225 and Ka4=26855

Dimer to Tetramer, with Ka2=34.687 with a variance=0.63951

Dimer to Hexamer, with a variance =0.56722 and Ka3=83.972

Trimer to Hexamer, with a variance =0.64872 and Ka2=1.349

Monomer to Tetramer:

Flow N=4 and Ka4, we got N=~6, with a variance=0.55565, perhaps indicating monomer can take the path and directly assemble to hexamer with a ka4 (Ka6=131067.6)

Dimer to Hexamer:

Flow N=3 and Ka3, we got N=~4.26, indicating dimer can go thru Tetramer with variance =0.54738, indicating that dimer can also assemble to tetramer (~4.26N) with a ka=820.4

Dimer to Tetramer to Hexamer:

Flow ka2 first to get Ka2=34.7, variance=0.63951.  Then uncheck Ka2 but kept its value and then flow Ka3, toe Ka3= 42.1 with a variance =0.63537., indicating dimer can form Tetramer and finally form Hexamer

If I flow both Ka2 and Ka3, but kept the values, then I got an ATTENTION! Window, with Error number: 5-Too many loops without convergence. Message

Summary of model fitting:

The protein is in 25 mM HEPES, 0.1mMEGTA, 200mM KCl, and SV and SE experiment was carried at 4C.

Monomer~91KD, Dimer~182KD, Trimer~273KD, Tetramer~364KD, Pentamer~455KD, Hexamer~546KD

Use v-bar=0.7167, rho=1.0084, viscosity=1.0064E-2 (all values are obtained from SEDNTERP but omitted contribution of HEPES and EGTA)

Selected subset range radius from ~6.9cm to 7.12cm to make the comparison more meaningful and more consistence.

| Model | Origin Variance, Ka(abs) | Comment |
| --- | --- | --- |
| Monomer to Trimer | 0.7347, 26855 |  |
| Monomer to Tetramer | 0.61225, 6.98E78 |  |
| Dimer to Tetramer | 0.63951, 131068 |  |
| Dimer to Hexamer, | 0.56722, 84 |  |
| Trimer to Hexamer | 0.64872, 1.35 |  |
| Monomer to Tetramer but flow N4and K4 We actually converge Monomer to Hexamer | 0.54738, 131068 | N4 flow to 5.97(~6) with Ka=131068 |
| Dimer to Hexamer but flow N3and K3 We actually converge Dimer to Tetramer | 0.54738, 820 | N3 flow to 4.26(~4) with Ka=820 |
| Dimer to Tetramer to Hexamer: | 0.63537 with K2=34.7, Ka3=42.1 | Flow ka2 first to get Ka2=34.7, variance=0.63951. Then uncheck Ka2 but kept its value and then flow Ka3 , to Ka3= 42.1 with a variance =0.63537., indicating Dimer can form Tetramer and finally form Hexamer |

Using variance (goodness of fit) as a guide, the results indicate that the association processes to form Hexamer involve Monomer, Dimer and Tetramer. This conclusion can also be support by the SV experiment while one can almost visualize each species in solution.